## Slide 1: REAL-TIME DIRECTIONAL ANTENNA ALIGNMENT USING REINFORCEMENT LEARNING AND RSSI FEEDBACK Atul Tiwari (THA079BEI006) Bibek Joshi (THA079BEI007) Inisha Maharjan (THA079BEI012) Suprim Koirala (THA079BEI043) Supervisor: Er. Saroj Shakya Department of Electronics and Computer Engineering Institute of Engineering, Thapathali Campus March 29, 2026

## Slide 2: Presentation Outline
Motivation
Introduction
Objectives
Scope of Project
Methodology
Results
Analysis of Results
Future Enhancements
Project Applications
Conclusion
Appendices
References

## Slide 3: Introduction
Directional antennas focus energy to improve SNR & range
Alignment crucial for reliable communication
Manual alignment is time-consuming and error-prone
Existing automated methods require costly RF hardware
Low-cost, RSSI-based autonomous alignment is needed

## Slide 4: Motivation
Figure: Image Generated by NanoBanana (Gemini)

## Slide 5: Objectives
To design and implement a low-cost embedded system capable of measuring RSSI in real time and mechanically steering a directional antenna
To develop and evaluate lightweight reinforcement learning-based alignment strategies, comparing their performance against baseline methods

## Slide 6: Scope of Project
Capabilities
  Implement stepper-controlled antenna using microcontroller
  Develop baseline RSSI scanning and hill-climb algorithms
  Integrate lightweight reinforcement learning for antenna control
  Evaluate performance in static and dynamic environments
Limitations
  Advanced multi-antenna systems like MIMO, phased arrays
  High-frequency mm-Wave and beamforming techniques
  Transmitter-side adaptation or coordinated alignment
  Full mobility and high-speed movement scenarios
  RSSI variability limits experimental repeatability

## Slide 7: Methodology (1) System Block Diagram

## Slide 8: Methodology (2) Hardware Implementation
Antenna: High-gain directional Yagi PCB Type.
Processor: ESP32-S3 for logic execution.
Actuator: NEMA 17 Stepper Motor for precision.
Driver: A4988 driver for smooth motor control.
Power: External 12V supply for motor torque.

## Slide 9: Methodology (3) Source and Receiver Configuration
Transmitter Node​
ESP32 microcontroller​
Directional antenna​
Periodic Data Transfer
Receiver Node​
ESP32 microcontroller​
Directional antenna​
Stepper motor assembly
Alignment Algorithm

## Slide 10: Methodology (4) Software Implementation
Arduino IDE and PlatformIO with ESP32-S3 Core
Embedded C/C++ Firmware Development
Lightweight Q-Learning Algorithm
Serial Monitor and Plotter
Python for Data Analysis, Simulation
Matplotlib for Data Visualization, KiCad for circuit diagrams

## Slide 11: Methodology (5) System Flow Diagram

## Slide 12: Methodology (6) Baseline Methods
Exhaustive angular scanning
This approach maps the entire search space to find the absolute best location, providing high accuracy but low efficiency.
RSSI-based hill-climbing
This method starts at a random point and iteratively moves to adjacent points with higher RSSI values until it hits a local maximum. It is fast but can get trapped in local maxima.

## Slide 13: Methodology (7) Reinforcement Learning Overview
Model-free control paradigm
Learn from interaction & rewards
Optimize antenna orientation over time
Tabular Q-Learning
Suitable for low-cost embedded systems

## Slide 14: Methodology (8) RL Model Design

## Slide 15: Methodology (9) RL Control Flow

## Slide 16: Methodology (10) Reinforcement Learning Framework
State Space:
  Current RSSI level and signal trend.
  Current angular position of the antenna.
  Thresholds classify RSSI increase/decrease/stable
Action Space:
  Rotate clockwise, counter-clockwise, or stay.
  Step size trade-off: precision vs. speed
Reward Function:
  Positive reward for increased signal strength.
  Penalty for signal drops or unnecessary movement.

## Slide 17: Methodology (11) RL Limitations
Dependence on discretization
Generalization limits
Sensitivity to the training environment

## Slide 18: Methodology (12) Experimental Setup
Indoor lab/corridor for multipath testing
Outdoor line-of-sight environment
Random initial antenna misalignment
Repeated trials (N ≥ 10) for reliability

## Slide 19: Methodology (13) Evaluation Metrics
RSSI (primary signal strength)
Movement Count
Convergence Time ​
Success Rate
RSSI Variability

## Slide 20: Results (1) Exhaustive Scanning
Global maximum RSSI of −30.14 dBm at an antenna orientation of (𝜃pan, 𝜃tilt) = (88°, 90°)
945 mechanical steps and 18900 RSSI samples
Approximately 67.7 seconds of convergence time

## Slide 21: Results (2) Hill Climbing

## Slide 22: Results (3) Hill Climbing at Bad Initialization

## Slide 23: Results (4) RL Learning Convergence

## Slide 24: Results (5) RL Performance

## Slide 25: Results (6) Average Simulation Performance
Metric | Exhaustive Scan | Hill Climbing | Q-Learning
Best RSSI Achieved (dBm) | -30.14 | -32.13 | −30.82
Optimal Pan Angle (deg) | 88 | 90 | 90
Optimal Tilt Angle (deg) | 90 | 86 | 90
Convergence Time (s) | 67.68 | 6.51 | 5.51
Number of Steps Taken | 945 | 39 | 25
Total RSSI Samples | 18,900 | 780 | 500
Initialization Sensitivity | None | High | Low
Ability to Escape Local Maxima | Not Applicable | No | Yes
Suitability for Embedded Use | Low | Medium | High

## Slide 26: Results (7) PCB and Slip-Ring Design

## Slide 27: Results (8) Hardware Design

## Slide 28: Results (9) Average Practical Performance
Method | Avg. RSSI (dBm) | Avg. Time (s) | Avg. Moves | Success (%) | RSSI Std. Deviation (dB)
Exhaustive | -49.95 | 54.20 | 812 | 100 | 1.60
Hill-Climbing | -52.73 | 11.84 | 63 | 80 | 2.34
Q-Learning | -49.55 | 9.62 | 57 | 95 | 1.28

## Slide 29: Results (10) Average Practical Performance

## Slide 30: Analysis of Results (1)
RL learns directional correlation instead of brute-force search
RL Utilizes historical RSSI trends for decision making
RL Avoids repeated exploration of low-reward orientations
Exhaustive Scan guarantees global optimum
Hill Climbing converges faster but is sensitive to the initial antenna orientation

## Slide 31: Analysis of Results (2) Simulation to Practical Deviation
Method | Simulation RSSI (Avg.) | Practical RSSI (Avg.) | ΔRSSI (dB) | Simulation Time (s) | Practical Time (s) | ΔTime
Exhaustive Scanning | -30.14 | -48.95 | -18.75 | 67.68 | 70.20 | 3.6%
Hill-Climbing | -32.13 | -52.73 | -22.60 | 6.51 | 11.84 | 81.9%
Q-Learning (RL) | -30.82 | -49.55 | -19.73 | 5.51 | 9.62 | 74.6%

## Slide 32: Future Enhancements
Mechanical and Hardware Improvements
Algorithmic Improvements
Embedded Software Enhancements
System-Level Extensions

## Slide 33: Project Applications
Improving reliability and range of fixed wireless links
Enhancing signal stability in IoT or sensor networks with directional antennas
Low cost point-to-point wireless communication systems where manual alignment is impractical
Educational and research platforms for exploring embedded RL in real-time RF control

## Slide 34: Conclusion
Successfully implemented autonomous antenna alignment using ESP32-S3 and Q-learning
RL reduced alignment time by 82.25% compared to exhaustive scanning
Offers useful time-accuracy trade-off rather than absolute RSSI superiority
Lightweight 12.3 kB Q-table fits easily within embedded memory constraints
Discrete state-space may miss optimal alignments between sampled angles

## Slide 35: Appendix - I [Gantt Chart]

## Slide 36: Appendix - II

## Slide 37: References I
[1] C. Beard and W. Stallings, Wireless Communication Networks and Systems. Pearson, 2016.
[2] S. Ahmed et al., “Comparative analysis of machine learning algorithms for antenna alignments,” IEEE Access, 2021.
[3] A. T. Koru, J. Chang, and Y. Wan, “RSSI-based distributed control to align directional antenna pairs for UAV communication,” IEEE/ASME Transactions on Mechatronics, 2024.
[4] Y. Wan et al., “Received signal strength indicator-based decentralized control for robust long-range aerial networking using directional antennas,” IEEE Transactions on Aerospace and Electronic Systems, 2018.

## Slide 38: References II
[5] J. W. Smith et al., “SmartAntenna: Enhancing wireless range with autonomous orientation,” International Journal of Distributed Sensor Networks, 2019.
[6] Á. L. Makara, B. T. Csathó, A. Rácz, T. Borsos, L. Csurgai-Horváth, and B. P. Horváth, “Deep-Learning-Based Antenna Alignment Prediction for Mobile Indoor Communication,” Sensors, vol. 23, no. 7, p. 3375, 2023, doi: 10.3390/s23073375.
[7] R. S. Sutton and A. G. Barto, Reinforcement Learning: An Introduction, 2nd ed. Cambridge, MA, USA: MIT Press, 2018. ISBN 978-0262039246.